Introduction

The goal of this proposal is to standardize, within the P4 community, header definitions for some of the most common headers specified in public RFC and IEEE specifications. The aim of portable P4 Headers (PPH) is to ease the portability and interoperability of P4 programs written by the community, and to make it easier for P4 developers to focus on their specific application needs, instead of writing standard headers. While P4 programs are typically not compatible across different target architectures, PPH aims to help improve the readability and understanding of P4 programs for those interested in sharing their P4 programs publicly.

The PPH proposal will focus on common
- header type names
- field names
- field name sizes
- typedefs for standard fields
- consts for standard field values

PPH considers only the P4-16 language definition specification.

Non-goals of this PPH proposal include
- Requiring any P4 developer to conform to the PPH coding style
- Prohibiting any P4 developer from using only part of the PPH
- Prohibiting any P4 developer from forking, extending or modifying the PPH

The PPH proposal is based on a collection of open source examples of P4 source code, gathered across the industry and academia (summer 2021), and will be published by P4.org under the Apache 2.0 license. Any exclusion is not intentional, and all contributions are welcomed.
The proposed P4 header source files will consist primarily of P4_16 `header` type
definitions, but likely also common `const` and `enum` definitions for relevant values of fields such as Ethernet protocol values and IPv4 protocol / IPv6 Next header values.

The headers will be restricted to those often used in networking, with public RFC or IEEE specifications. They will focus on the fixed-length fixed-format portions of those headers, given that the current state of the art P4 implementations often handle those via `varbit` fields, without parsing their internal structure. For example, they will include one definition of a TCP header that is exactly 20 bytes long, since many P4 programs do not need to parse
TCP options, and another TCP header definition that starts with those same 20 bytes, followed by a `varbit` field that includes all of the possible TCP options (up to 40 bytes long).

There will be no header definitions that are proprietary to any company included in these header files published by P4.org, unless that company chooses to include them and release their definitions under the appropriate license. There will be no mentions of specifics of particular P4 target or compilers, unless the vendors of those targets/compilers choose to publish them. There will be no trade secret or proprietary information of any kind included in PPH.

Users of PPH should feel free to create their own header definitions that are different from the published ones in areas where different P4 implementations have different limitations, bugs, or suggested workarounds that compile better on a specific target device. Examples of such areas include:

- IPv6 extension headers
- Whether to include IPv4 options in the IPv4 header definition or keep them separate. The published files will include one definition of an IPv4 header that has no IPv4 options at all, and a separate IPv4-with-options header type definition that does include the options as a single `varbit` field.
- Whether the IPv4 header has (a) a single 16-bit field for reserved+MF+DF+fragment offset fields, or (b) a 3-bit field and a 13-bit field, or (c) 3 1-bit fields and a 13-bit field, etc.
- Use of header unions to denote headers that are mutually exclusive.

Additional header definitions, used to assist in parsing the internal structure of IPv4 options, may be addressed in a future version of these files. Where the P4 developer decides to modify a PPH header (e.g. given performance/restrictions of a current P4 target or compiler) it is recommended that the different variant be created by
- Copying the header definition in the P4.org published file
- Rename its type to something unique to the target specific code base
- Change only the field definitions that are needed, leaving the names and types of the others as they are, so they share as much in common with the public header definitions as possible
Code style survey
There are multiple types of coding styles. It appears P4 developers are most commonly influenced by C and C++ styles (e.g. from programming software dataplanes and kernel modules), but also Java from the control plane (e.g. ONOS). The main choices are camel case and snake_case with some suffix variations. The following data was obtained from 12 different sources, 6 from industry and 6 from open source/academic sources.

Headers
Headers
standard_header_h	StandardHeader_h	std_hdr_t	standard_header_t
17%	8%	8%	67%

The most common headers and name style are:

ethernet_t	vlan_tag_t
ipv4_t	ipv6_t
gre_t
udp_t	tcp_t
vxlan_t	vxlan_gpe_t

icmp_t	arp_t

Header Fields
Fields
ether_type	etherType	e_type	ethernetType
42%	16%	21%	21%

Again, the most common style is snake_case, with mostly the full word used instead of an abbreviation. Five of these sources contained a mix of CamelCase and snake_case, which seems to be an oversight: e.g. where CamelCase is expected (srcPort, dataOffset and urgentPtr) and occasional snake_case slips in (options_ts).
Constants:

Pretty much all the sources choose:

const bit<16> ETHERTYPE_IPV4 = 0x0800;
const bit<16> ETHERTYPE_ARP = 0x0806;

Typedefs:

Most of the industry vendors use typedefs. Half of all headers use typedefs with snake case
typedef bit<48> mac_addr_t;
typedef bit<12> vlan_id_t;
typedef bit<32> ipv4_addr_t;
typedef bit<16> l4_port_t;

versus

typedef bit<48> EthernetAddress;
typedef bit<32> IPv4Address;
typedef bit<128> IPv6Address;

Typedefs
ether_type_t	ethernetType
60%	40%

The most common was snake_case style, along with an “_t” type identifier at the end. Fortunately no one uses hungarian notation.

Unions
Three vendors are using union types

header_union ip_h {
  ipv4_t ipv4;
  ipv6_t ipv6;
}

header_union l4_uh {
    udp_h udp;
    tcp_h tcp;
    icmp_h icmpv4;
    icmp_h icmpv6;
}

This one is interesting, because aside from adding an extra layer of syntax (hdr.ip.ipv4), it potentially allows the compiler to optimize extractions since it explicitly signals that these two header types cannot occur at the same time (at the same offset), just like in C

Enums
None of the contributed P4 source used enums, serializable or regular

A Proposed Code style

Type	Syntax	Description
Headers	standard_header_t	snake_case, with “_t” identifier at the end. While not a majority, seems better so as not to mix with typedefs (below). / Prefer lengthier description rather than terse abbreviations
Header fields	standard_field	snake_case, with lengthier name rather than abbreviation
Constant field values	UPPER_CASE	Uppercase snake_case, prefer P4 const with type rather than #define
Typedefs	standard _type_t	Snake_case with “_t” identifier. Usage varies
Header Union	ip_h	Snake_case with “_h”. / However, this may have other implications other than coding style.

Here are some basic examples, focusing on the most common headers and field layouts.
.
Note - fields which can potentially have finer granularity (e.g individual flag bits), or variable size TLVs have not been addressed. List of typedefs, consts and headers are not complete, but shown as a general example of style

// Some common field types
typedef bit<48> mac_address_t;
typedef bit<12> vlan_id_t;
typedef bit<32> ipv4_address_t;
typedef bit<128> ipv6_address_t;
typedef bit<24> vni_t;

// Some typical ether_types
const bit<16> ETHERTYPE_MAC = 0x6558;
const bit<16> ETHERTYPE_IPV4 = 0x0800;
const bit<16> ETHERTYPE_IPV6 = 0x86DD;

header ethernet_t
{
    mac_address_t dst_addr;
    mac_address_t src_addr;
    bit<16> ether_type;
}

header vlan_tag_t {
    bit<3> pcp;
    bit<1> dei;
    vlan_id_t vlan_id;
    bit<16> ether_type;
}

header ipv4_t {
    bit<4> version;
    bit<4> ihl;
    bit<8> diffserv;
    bit<16> total_length;
    bit<16> identification;
    bit<3> flags;
    bit<13> frag_offset;
    bit<8> ttl;
    bit<8> protocol;
    bit<16> header_checksum;
    ipv4_address_t src_addr;
    ipv4_address_t dst_addr;
}

header ipv4_option_t {
    bit<8> type;
    bit<8> length;
    bit<16> value;
}

header ipv6_t {
    bit<4> version;
    bit<8> traffic_class;
    bit<20> flow_label;
    bit<16> payload_length;
    bit<8> next_header;
    bit<8> hop_limit;
    ipv6_address_t src_addr;
    ipv6_address_t dst_addr;
}

header_union ip_t {
  ipv4_t v4;
  ipv6_t v6;
}

header mpls_t {
    bit<20> label;
    bit<3> tc;
    bit<1> bos;
    bit<8> ttl;
}

header icmp_t {
    bit<8> type;
    bit<8> code;
    bit<16> checksum;
    // ICMP payload is not parsed
}

header udp_t {
    bit<16> src_port;
    bit<16> dst_port;
    bit<16> length;
    bit<16> checksum;
}

header tcp_t {
    bit<16> src_port;
    bit<16> dst_port;
    bit<32> seq_no;
    bit<32> ack_no;
    bit<4> data_offset;
    bit<4> res;
    bit<3> ecn;
    bit<6> flags;
    bit<16> window;
    bit<16> checksum;
    bit<16> urgent_ptr;
}

header vxlan_t {
    bit<8> flags;
    bit<24> reserved;
    bit<24> vni;
    bit<8> reserved2;
}

header vxlan_gpe_t {
    bit<8> flags;
    bit<16> reserved;
    bit<8> next_proto;
    bit<24> vni;
    bit<8> reserved2;
}

header gre_t {
    bit<1> checksum_present;
    bit<1> routing_present;
    bit<1> key_present;
    bit<1> sequence_present;
    bit<1> strict_source_route;
    bit<3> recursion_control;
    bit<5> flags;
    bit<3> version;
    bit<16> protocol;
}

header nvgre_t {
    bit<24> vsid;
    bit<8> flow_id;
}